## Slide 1: Aviation Safety Margins
Application to Aircraft Operations

## Slide 2: Takeoff Example
Aircraft Rotation: 100 knots
Acceleration: 25 knots per 1,000 feet
Deceleration: 25 knots per 1,000 feet
= 1,000 feet
25 knot headwind
10,000 feet
Rotation
Takeoff Roll
Abort Distance
Safety Margin

## Slide 3: Takeoff Example
Aircraft Rotation: 100 knots
Acceleration: 25 knots per 1,000 feet
Deceleration: 25 knots per 1,000 feet
= 1,000 feet
No wind
10,000 feet
Rotation
Takeoff Roll
Abort Distance
Safety Margin
(reduced by 50%)

## Slide 4: Takeoff Example
Aircraft Rotation: 100 knots
Acceleration: 25 knots per 1,000 feet
Deceleration: 25 knots per 1,000 feet
= 1,000 feet
No wind
8,000 feet
Rotation
Takeoff Roll
Abort Distance
No safety margin
(safety margin depleted)

## Slide 5: Takeoff Example
Aircraft Rotation: 100 knots
Acceleration: 25 knots per 1,000 feet
Deceleration: 25 knots per 1,000 feet
= 1,000 feet
No wind
6,000 feet
Rotation
Takeoff Roll
Abort Distance
Negative safety margin
Refusal Speed
Abort Distance